## Slide 1
Bio Energy
Renewable Energy Technology

## Slide 2
Biofuel Potential
The highest-grade fuels are the liquid or gaseous ones. Biofuels in a liquid or gaseous form are far more valuable than solid biomass.
Biomass is produced via photosynthesis (very low-efficient process) and is ultimately a concentrated solar energy.
Biomass alone can NOT be a single source of both fuel and food for the growing population on planet Earth. Efficient production, conversion, utilization methods should be required.
If the biofuel resource is available, it should be utilized efficiently while replacing the highest possible amount of fossil fuels.

## Slide 3
Biofuel Importance
Biomass can be managed sustainably in smaller scales.
Using biofuels in transportation is the first step towards the future sustainable society that would be based on hydrogen or synthetic fuels from renewable energy.
Biofuels are to a large extent able to utilize existing infrastructure and equipment for handling, storage, distribution and final use.

## Slide 4
Biofuel Classifications
First Generation Biofuels (1G): Produced from food-grade biomass by natural microbiological processes.
Example: Vegetable oils, Ethanol, Biogas from crops.
Very controversial the “food vs. fuel” debate!
1G Non-Food Biofuels: Produced by natural processes but from non-edible biomass, i.e. from organic residues, garbage.
Example: Biogas
Second Generation Biofuels (2G): Produced by advanced thermochemical conversion methods from non-edible biomass feedstocks.
Example: Alcohols or biosynthetic fuels from wood
2G biofuels aim to utilize a more sustainable feedstock and/or apply more efficient conversion methods.

## Slide 5
Biofuel Classifications
Third Generation Biofuels (3G): Based on more productive, special grown non-food biomass feedstocks.
Example: Algae, genetically modified or hybrid crops, artificial photosynthesis.
3G biofuels aim at enhancing the resource base by a more efficient photosynthetic process.
Fourth Generation Biofuels (4G): Scrubbing away CO2 from an already CO2 neutral biofuel or synthetic fuels from recycled carbon based on renewable energy.
4G biofuels would be carbon-negative and/or apply highly efficient direct conversion methods.

## Slide 6
Vegetable Oils
Vegetable oils (plant oils) are polyglycerides- a readily available natural fuel produced by certain plant species, replacement to fossil diesel.
Oil can be directly extracted from the fruits or seeds of the oil-producing plants by simple methods:
  Cold pressing followed by filtration or
  Warm pressing followed by extraction with organic solvents and purification.
Examples of plants with high oil content are:
Oil palm, sunflower, canola, soy, linseed, hemp, jojoba, jatropha, avocado and all kinds of nuts etc.
Canola is the oil plant of the north-temperate climate with yields of around 1-2 m3 of oil per hectare.

## Slide 7
Straight Oils vs. Biodiesel
Vegetable Oils can be used in two different forms:
    Raw Straight Vegetable Oils (SVO), the only treatment is filtering.
    Chemically converted into esters = Biodiesel
Use of SVO in burners or engines is difficult due to high viscosity, danger of polymerization, wax sedimentation, coking at fuel injectors, solidification at low temperatures etc.
Engine conversion/adaptation is necessary if SVO is the fuel.
Biodiesel solves some SVO-related problems by having physical properties very similar to those of fossil diesel, however certain major problems remain plus that the presence of methanol and alkali residues in biodiesel might also be a problem for engines not adapted to the fuel.

## Slide 8
Biodiesel
Biodiesel production is a chemical process for trans-esterification of the complex triglyceride molecule of vegetable oil.
The result is a mixture of fatty esters with properties close to fossil diesel.
The biggest disadvantage of biodiesel is its higher cost than SVO.

## Slide 9
Biodiesel
Advantages:
  Perfect diesel substitute, can be used in all types of diesel engines.
  Has heating value close to that of fossil diesel.
  Possible to produce in small scales with batch processes.
  Can be produced also from refuse fats, animal fats or discarded cooking oils.
Disadvantages:
  May contain residues of methanol or alkali catalyst.
  Still susceptible to aging or freezing just like SVO.
  Difficult to maintain the production process in small scales.
  Much more expensive than the raw SVO.

## Slide 10
SVO as Diesel Substitute
Advantages:
  Directly delivered by oil plants. Simple and cheap biofuel.
  Can easily be produced and used at small scales i.e. free from centralized manufacturing or from political/corporate misuse.
Disadvantages:
  High viscosity and prone to waxing, coking, freezing, aging.
  Difficult cold start to the engine, cokes on injectors or valves.
  Engines need to be specially converted/adopted as SVO.

## Slide 11
SVO as Diesel Substitute
Way to solve the problems:
Preheat the SVO before it reaches the engine by adding a simple heat exchanger along the fuel line.
Upgrade of injectors and/or fuel pumps for cold-starting on 100% SVO.
Avoid using SVO older than 2 years, store in dark and ventilated rooms.
Double-tank solution- cold start on diesel then switch to SVO
Combustion Characteristics:
Both SVO and biodiesel behave in the same way and produce the same pollutant emissions as fossil diesel fuel when combusted.

## Slide 12
SVO as Diesel Substitute
Way to solve the problems:
Preheat the SVO before it reaches the engine by adding a simple heat exchanger along the fuel line.
Upgrade of injectors and/or fuel pumps for cold-starting on 100% SVO.
Avoid using SVO older than 2 years, store in dark and ventilated rooms.
Double-tank solution- cold start on diesel then switch to SVO
Combustion Characteristics:
Both SVO and biodiesel behave in the same way and produce the same pollutant emissions as fossil diesel fuel when combusted.

## Slide 13
Biogas Production
A simplified stoichiometry for anaerobic digestion of biomass is:
C6H10O5 + H2O 3 CH4 + 3 CO2
The process is based on the breakdown of the organic macro-molecules of biomass by naturally occurring micro-organisms, through the following four steps:
  Hydrolysis: Polymers such as cellulose, starch, proteins and lipids are hydrolyzed to soluble compounds (monomers) such as sugars.
  Fermentation: Soluble compounds are converted to different compounds such as amino acids, fatty acids, alcohols, CO2, H2, NH3 and H2S.
  Acetogenesis: Fermentation products are then converted to a mixture of hydrogen, low molecular weight acids (primarily acetic acid) and carbon dioxide.
  Methanogenesis: Products of the acetogenesis step are reacted together to produce methane.

## Slide 14
Biogas Production

## Slide 15
Biogas Yield
Around 50-60% of the initial energy content in the organic material can be converted to biogas in a properly operated digester.
The resultant gas mixture consists of CH4 (60-65%), CO2 (the rest) and small amounts of water vapors, H2S, NH3 and some organic that give bad odor.
The gas is a ready fuel for stationary CHP boilers or piston engines but should be cleaned and upgraded to minimum 95% methane if used as automotive fuel.

## Slide 16
Biomass
Renewable Energy Technology

## Slide 17
Biomass
Biomass energy is derived from plant and animal material, such as wood from forests, residues from agricultural and forestry processes and industrial, human or animal wastes.
The energy value of biomass from plant matter originally comes from solar energy through the process known as photosynthesis:
  6CO2 + 6H2O + light energy = C6H12O6 + 6O2

## Slide 18
Photosynthesis
Fig. Inputs and outputs of the photosynthetic process.
The chemical energy that is stored in plants and animals, or in the wastes that they produce, is called bioenergy.
Essentially, the use of biomass for energy is the reversal of photosynthesis.

## Slide 19
Biomass Contd…
The net energy available in the biomass when it is combusted ranges from
  About 8MJ/kg for green wood to 20MJ/kg for oven dry plant matter,
Compared to 55MJ/kg for methane; and about 23 - 30MJ/kg for coal
Biomass Resources for energy production cover a wide range of materials:
  Agricultural crops: sugar cane, corn, wheat, sorghum, etc.
  Vegetable oil bearing crops: sunflowers, rapeseed, soybean, palm etc.
  Agricultural residues: rice husk, bagasse, coconut husk and shell, palm oil fiber, rice straw, jute straw etc.
  Forestry crops and residues
  Animal waste
  Municipal waste

## Slide 20
Biomass Contd…
Biomass Conversion Technologies:
  Anaerobic digestion
  Briquetting and pellestising
  Direct combustion
  Pyrolysis
  Gasification
  Charcoal production
  Ethanol production
Biomass Applications:
  Biofuels
  Electricity generation
  Heat and steam generation
  Combustible gas

## Slide 21
Virgin Biomass
Almost all plant life on Earth can be broken into three categories based on the way they assimilate carbon dioxide into their systems: C3, C4 and CAM plants.
C3 plants include more than 95% of the plant species on earth. (Trees, for example, are C3 plants.)
C4 plants include such plants as sugarcane and corn. They are the second most dominant photosynthetic type.
During the first steps in CO2 assimilation, C3 plants form a pair of three carbon atom molecules.
C4 plants, on the other hand, initially form four carbon-atom molecules
The important difference between C3 and C4 species for rising CO2 levels is that C3 species continue to increase photosynthesis with rising CO2, while C4 species do not.

## Slide 22
Virgin Biomass
C3 plants tend to grow well in areas where:
  Sunlight intensity is moderate, Temperatures are moderate (15-25 °C)
  High CO2 compensation point. CO2 compensations point is the point at which more CO2 is breathed than normal.
  Ground water is plentiful
C4 plants have a competitive advantage over C3 pathway under conditions of:
  Drought,
  High temperatures (30-40 °C)
  Low CO2 compensation point

## Slide 23
Aquatic Biomass as Energy Resource
There are a variety of aquatic biomass resources, such as algae, giant kelp, other seaweed, and marine microflora.
  Most efficient in photosynthesis
  Do not have any commercial use
The aquatic alternative can be used in:
  Biomass production
  Waste treatment
  Conversion to fuels by fermentation

## Slide 24
Waste Biomass as Energy Resource
Waste biomass is energy-containing material that is, discarded, disposed of and that are mainly derived from or have their origin in virgin biomass and could be used as fuel for production of steam and electric power.
MSW (Municipality Solid Waste) is inherently a blended fuel, and its major components are paper (43%); yard waste, including grass clippings (10%); food (10%); glass and ceramics (9%); ferrous materials (6%); and plastics and rubber (5%).
MSW can decompose in two ways, aerobic and anaerobic.
Aerobic decomposition (or composting) occurs when O2 is present. The composting produces CO2 and water, but no usable energy products.
The anaerobic decomposition occurs in the absence of O2. It produces landfill gas of 55% CH4 and 45% CO2.
Waste Biomass is lower in cost than virgin and often you can be paid to take away waste biomass with negative cost.

## Slide 25
Biomass Constituents
Biomass contains the elements-
  Carbon (45-55 weight %),
  Hydrogen (5-7 weight %),
  Oxygen (40-50 weight%) and
  Small amounts of sulfur (0-0.05 weight %) and
  Nitrogen (0-1.0 weight %).
The compositional differences in biomass are large:
Heating value
Moisture content
Ash content

## Slide 26
The Need of Biomass Refinement
Utilization of pre-treatment facilities for biomass is totally dependent on the biomass-to-energy efficiency.
Thus, the interest, today lies in energy densification of biomass to a high energy efficient, easy fed fuel for combustion, co-combustion and gasification applications
Many of the problems with wood gasification are related to the properties of the fuel that is thermally unstable, which may lead to formation of condensable tars
Additionally, higher gasification efficiency can be achieved by fuels with lower O/C ratio.

## Slide 27
The Need of Biomass Refinement
Utilization of pre-treatment facilities for biomass is totally dependent on the biomass-to-energy efficiency.
Thus, the interest, today lies in energy densification of biomass to a high energy efficient, easy fed fuel for combustion, co-combustion and gasification applications
Many of the problems with wood gasification are related to the properties of the fuel that is thermally unstable, which may lead to formation of condensable tars
Additionally, higher gasification efficiency can be achieved by fuels with lower O/C ratio.

## Slide 28
Biomass Refinement
The physical conversion technology includes-
  Dewatering
  Drying
  Size reduction
  Densification
  Separation
  Torrefaction

## Slide 29
Case Study: Rice Husk Gasifier based Power Generation in Bangladesh
250 kW Rice Husk gasifier power plant
Location: Kapasia, Gazipur
Capacity : 250 kW
Engine : Diesel converted to dual-fuel mode
Fuel : 300 kg Rice Husk/hr
Gas-diesel ratio: 70:30
Total cost: 2.5 crore
Beneficiary: 200 household and 100 commercial user

## Slide 30
Existing Practice of Rice Husk Energy Use for Parboiling system
Rice Processing zone at Munshiganj
Traditional steam producing system for rice parboiling in Bangladesh
In Bangladesh, 90% of rice is parboiled, It needs huge amount of thermal energy, Rice husk is mainly used for steam generation in rice parboiling system

## Slide 31
Efficient Use Rice Parboiling System (BRRI-GTZ initiative)
Improved rice parboiling system
Location: Kaliakoir, Gazipur
Parboiling Capacity : 18 ton paddy /batch
Fuel : Rice Husk
Efficiency : 47 – 50%
Fuel savings : 900 kg husk/batch
CO content in Flue gas: 100-500 ppm
About 2 million ton of rice husk could be saved every year in Bangladesh if the rice millers would adopt this improved rice parboiling system

## Slide 32
Improved Biomass Cook Stove
Efficiency of traditional stoves is 8-10%
Improved Cook Stoves (ICS) can easily achieve a thermal efficiency of 20%
ICS
Village Restaurant
Source: Ijaz Hossain 2010